## Slide 1
Efficient Ray Tracing of Parametric Surfaces for Advanced Effects
Rohit Nigam, P. J. Narayanan
CVIT, IIIT Hyderabad, Hyderabad, India

## Slide 2: Ray Tracing
Render visually realistic images
Rays start from camera center and move through every pixel
Final color value calculated from intersection with different objects in the scene
High visual realism, but at a much higher computational cost.
image obtained from
siliconarts.co.kr

## Slide 3: GPU and Hybrid Computing
GPUs are used for many compute intensive problems(GPGPU)
Nvidia GTX 680 has 1536 CUDA cores and can processing power of upto 3.1 TFLOPS.
Processing power of CPU cores have also increased along with their numbers
GPUs are suitable for parallelizable tasks, while CPU works faster for serialized operations.
A hybrid operation uses both GPU and CPU cores to perform compute intensive operations.

## Slide 4
Representing a Scene
Triangular Mesh
f>0
f<0
f=0
Implicit Surface
Parametric Surface

## Slide 5
Parametric Surface: Motivation
Provide compact and effective representation.
Remain curved and smooth at arbitrary level of zooming.
Memory efficient, in comparison with triangular mesh.
image obtained from
uni-weimar.de

## Slide 6
Bezier Surfaces
Most basic form of parametric surfaces
Described as:
  Q(u,v) = [U][M][P][M]T[V]T
  where [U] = [u3 u2 u 1] and [V] = [v3 v2 v 1], 0 ≤ u,v ≤ 1
  [M] : Bezier Basis Matrix
  [P] : set of 16 Control Points defining the patch

## Slide 7
Rendering Bezier Surfaces
Tessellation based approches
  Eisenacher et al.(2009) :
  View Dependent Adaptive Subdivision
Direct Ray Tracing
  Geimer et al.(2005) :
  Newton Iteration
  Pabst et al.(2006) :
  Bezier Clipping + Newton Iteration

## Slide 8
Rendering Bezier Surfaces
Kajiya’s Method
  Ray represented as two orthogonal planes
  Generates an 18 degree polynomial, solved using Laguerre’s method
  Lahabar implemented Kajiya’s algorithm on GPU to solve for intersections

## Slide 9
Ray Tracing Bezier Surface
Constructing an Accelaration Structure
  Grid
  KD-Tree
  Bounding Volume Hierarchy(BVH)
image obtained from
uva.onlinejudge.org

## Slide 10
Ray Traversal through BVH
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Ray List
Outputs
Potential Ray-Patch intersections list
Initial parameter values
Ray Tracing Bezier Surface

## Slide 11
Ray Tracing Bezier Surface
Newton Iteration
Bivariate Newton Iteration
to solve for (u,v)
  R is the intersection equation for a ray,
  J is the Jacobian matrix of R.
Picture Courtesy : http://steadyserverpages.com

## Slide 12
Geimer 2005
Based on the flatness criteria, each patch is divided into subpatches.
BVH for original surfaces
  Bounding boxes of subpatches at leaf nodes.
For each potential intersection
  Generate initial values for Newton Iteration
Achieve 6.4 fps for 512x512 image.
Original Curve
Subdivided Linear
Curve
BVH Nodes
1
2
3
sp1
sp2
sp1
sp2
sp1
sp2
Subpatches at Leaf
Patch1
P2
P3

## Slide 13
Our Approach
Mixed hierarchy: consists of two hierarchical structures.
1
2
3
4
BVH for
Patches
Subpatch
Hierarchy
  Top level BVH: Bounding boxes of original patches.
  Leaf nodes represent the original Bezier Surfaces.
  Each Patch is divided into fixed size subpatches, hierarchically, using De Casteljau algorithm.
  Subtree for each patch from bounding boxes of the subdivided patches.

## Slide 14
Mixed Hierarchy Advantages
Tighter bounds of subpatch
  Eliminates more rays
  Better Initialization
Low Additional memory
  Intersection performed on original patches.
Better suited for the GPU
  Shared memory stores skip pointer and subpatch number.
1
2
3
4
BVH for
Patches
Subpatch
Hierarchy

## Slide 15: Mixed Hierarchy Advantages
Discard early in subpatches
  Store distance of a hit along the
  ray ‘t’
  Discard nodes with
  high ‘t’ value
  Utilize shared memory for ‘t’
We subdivide 6 times.
We discard back-facing patches to reduce the overall list for primary pass
1
2
3
4
BVH for
Patches
Subpatch
Hierarchy

## Slide 16
GPU Implementation
A kernel traverses the first level of the BVH.
  Atomic operations to provide scalability.
  Output: Potential (Ray,Patch) intersections
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Ray List
0,1 | 2,2 | 3,6 | 4,3 | 5,7 | 6,1 | 7,3
0,1 | 2,2 | 4,3 | 5,7 | 7,3
14 | 8 | 7 | 34 | 63
Potential Ray-Patch
Intersections
Initial values
Another kernel parallely processes the generated (ray,patch) list.
  Tighter subpatch bounding boxes leads to further pruning.
  Output:
    Reduced potential (Ray,Patch) intersections.
    Initial values for each intersection.

## Slide 17
GPU Implementation
Newton Iteration
  Each Ray-Patch intersection mapped to a thread
  Applied till convergence or max iteration
  Output: Hit-point and surface normal
  Takes 20-30% of the total time
0,1 | 2,2 | 4,3 | 5,7 | 7,3
14 | 8 | 7 | 34 | 63
Initial values
Potential Intersections
H1 | H2 | NH | H3 | H4
N1 | N2 | NH | N3 | N4
Hit Points
Surface Normals

## Slide 18
Primary rays do not take other surfaces present into consideration
Secondary rays provide more realism to CGI
Secondary ray tracing includes
  Shadow
  Reflection
  Refraction
Secondary Rays

## Slide 19
Secondary Rays
Generate direction from hit-point and surface normal.
Generate Ray List.
Apply the same algorithm for secondary Ray List.
Recurse for a fixed depth for reflection/refractions.
H1 | H2 | NH | H3 | H4
N1 | N2 | NH | N3 | N4
Secondary Rays
0 | 1 | 2 | 3
Final Color values
Intersection
Algorithm
C1 | C2 | C3 | C4

## Slide 20: Refraction
Occurs when light ray changes direction due to change in medium
Direction of refracted ray computed using Snell’s Law
Each refraction bounce requires 2x normal bounce

## Slide 21
Hybrid Ray Tracing
Generate Rays
rayTraceGPU
rayTraceCPU
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3 | 4 | 5
6 | 7
H1 | H2 | NH | H3
N1 | N2 | NH | N3
H4
N4
0 | 1 | 2 | 3
Ray List
Hit Point
Surface Normal
Secondary Ray List
CPU
GPU
CPU
GPU

## Slide 22
Results
Teapot Model
Fps : 64(115)*
Bigguy Model
Fps : 28.6(68.5)
Killeroo Model
Fps : 19.2(44.7)
2 Killeroos
Fps : 10.6(23)
9 Bigguys
Fps : 5.2(13)
System Specs
GTX 580 + i7 920
1024x1024
Primary + Shadow
+ Reflection
* : Figure in bracket gives Primary fps

## Slide 23
Results (Primary+Secondary)
Model | Patches | Total Frame Time(ms) |  | 
 |  | CPU | GPU | Hybrid
Teapot | 32 | 137 | 17.05 | 15.61
Bigguy | 3570 | 232 | 39.45 | 34.92
Killeroo | 11532 | 351 | 58.3 | 52.19
2 Killeroos | 23064 | 726 | 106.03 | 94.55
9 Bigguys | 32130 | 3107 | 196.79 | 191.81

## Slide 24: Results
Model | Pure GPU GTX 580 (ms) | Pure GPU Tesla K20c (ms) | Multi-GPU GTX 580 + C2050 (ms)
Teapot | 8.71 | 5.42 | 5.63
Bigguy | 14.59 | 10.61 | 9.84
Killeroo | 22.38 | 17.85 | 15.69
2 Killeroos | 42.29 | 34.19 | 28.75
9 Bigguys | 77.05 | 58.92 | 51.12
Rendering time comparison of Multi-GPU (GTX 580 + C2050) against
Pure GPU (GTX 580) for different models

## Slide 25: Comparison
We achieve about 15.4 fps on an Intel Core 2 duo 2.20 Ghz system for teapot scene with 512×512 resolution in comparison to Geimer, who got 6.1 fps on a dual processor PowerMac G5 2GHz processor.
Model | Kajiya (ms) | Improved Kajiya (ms) | Newton (ms)
Teapot | 71 | 12.59 | 1.62
Bigguy | 147 | 18.57 | 4.43
Killeroo | 164 | 21.26 | 6.76
Comparison of different methods, Kajiya’s Method implementation on GPU by
Lahabar, Improved Kajiya’s method by us and Newton Iteration. All the
results are taken on GTX 480 for same screen coverage and screen resolution 512 × 512.

## Slide 26: Rendering in parts
24 Bigguys rendered at 12 fps
for 512x512 resolution on Nvidia GTX 580

## Slide 27: Box Scene
Bigguys in a box scene with soft shadows, 16 light sources,
rendered at 512 × 512 resolution in 158.8 ms on GTX 580

## Slide 28: Soft Shadows
Bigguy in a box scene with soft shadows, reflection, 16 light sources,
rendered at 512 × 512 resolution in 167.4 ms on GTX 580

## Slide 29
Path Tracing
We extend our ray tracing approach to Global Illumination effects.
We use Cook’s approach
  Monte Carlo based Stochastic Sampling
  Sample image at appropriate non-uniformly spaced points.
Each pixel sampled for a user defined samples per pixel
-0.5,-0.5
0.5,0.5

## Slide 30
Path Tracing
Bigguy in a box: 400 spp, 512x512 resolution
Rendered in 75 secs

## Slide 31
Path Tracing
Bigguy in a box: 1000 spp, 512x512 resolution
Rendered in 165 secs

## Slide 32
Path Tracing
Bigguy in a box: 2000 spp, 512x512 resolution
Rendered in 323 secs

## Slide 33
Path Tracing
Bigguy in a box: 5000 spp, 512x512 resolution
Rendered in 14.4 mins

## Slide 34
Path Tracing
Bigguy in a box: 10000 spp, 512x512 resolution
Rendered in 28.5 mins

## Slide 35: Advance Effects
Apply advanced effects like ambient occlusion, depth of field etc. for Bezier surface
Render advanced effects using mixed hierarchy algorithm
First implementation to render Bezier patches with advanced effects

## Slide 36: Ambient Occlusion
Approximate the effect of environment lighting
Adds realism by enhancing small surface details, adding soft shadows
Deals with diffuse surface and diffuse lighting
Considers the geometry of the scene
Calculates the part of the environment visible to each point on the model, defined by
Vp() is the visibility function at p in direction of , is the surface normal and dω is the infinitesimal solid angle through the hemisphere .

## Slide 37: Ambient Occlusion
GPU Algorithm
  First pass consists of primary rays
  Generates primary intersection points
  Shoot a fixed amount of rays, in random directions passing through the hemisphere centered around surface normal, away from surface
  Generates a massively large ray list
  Ray list is divided into chunks, to be processed parallely on the GPU
  To optimize further, each chunk can be categorized by direction, point of origin to provide more coherence for GPU architecture.

## Slide 38: Results
Model | Samples per pixel | No of rays | Time (ms) | Time per ray (μs)
Bigguy | 1024 | 70908475 | 7954.6 | 0.112
Killeroo | 1024 | 96016875 | 14019.4 | 0.146
2 Killeroos | 64 | 12303395 | 2299.8 | 0.187
2 Killeroos | 1024 | 194015075 | 33069.7 | 0.170
9 Bigguys | 64 | 17386330 | 4537.7 | 0.261
9 Bigguys | 1024 | 274169050 | 65472.2 | 0.239

## Slide 39: Results
2 Killeroos: 1024 spp, 1024x1024 resolution
Rendered in 33 seconds

## Slide 40: Results
9 Bigguys: 1024 spp, 1024x1024 resolution
Rendered in 65 seconds

## Slide 41: Depth of Field
Ray Tracing
Depth of Field
Range of distance in focus of the camera
Objects to the front or back of this range appear out of focus.
Depth of Field increases the realism in an image.
We shoot rays from a circle, called Circle of Confusion(CoC) centered around origin
Here, n is number of rays, o is origin, pi is point on image plane, qi is point on circle of confusion

## Slide 42: Results
Model | Focus | CoC | Time (ms) | Time per ray (μs)
 | Far | 0.8 | 193 | 0.736
Bigguy | Near | 0.8 | 193 | 0.736
 | Near | 0.2 | 192 | 0.733
 | Far | 0.8 | 273.5 | 1.043
2 Bigguys | Near | 0.8 | 272.5 | 1.04
 | Near | 0.2 | 271 | 1.034

## Slide 43: Results

## Slide 44: Motion Blur
Dynamic scenes are produced by a sequence of still images
Motion blur is produced by motion of object during the time camera shutter is open
To generate motion blur, the scene needs to be sampled temporally also
Distribute the rays both spatially as well as temporally

## Slide 45: Results
Image rendered at 512 x 512 resolution,
for 10 time steps, one ray per time step, in 115 ms.

## Slide 46: Gloss
Objects not purely specular
Simulated by distributing rays around the reflection direction
Reflected ray direction calculated as
R is reflection direction, s is glossiness index, u and v are orthogonal to R, p,q are random numbers in [-1, 1]
Can model different surfaces by using BRDF.
PoC
Incident Ray
R

## Slide 47: Results
No of Rays | Rays per hit | Gloss | Time (ms) | Time per ray (μs)
270768585 | 4 | Low | 244.7 | 0.904
270768585 | 4 | Med | 248.9 | 0.919
270768585 | 4 | High | 252.1 | 0.931
990607950 | 16 | Med | 792.6 | 0.8
Gloss: Low
Gloss: Med
Gloss: High

## Slide 48: Results
Glossy reflections using 1000 samples per pixel and 16 reflection rays
for each intersection, rendered at 512 × 512 resolution with 0.4 as s value

## Slide 49
Conclusions
A mixed hierarchy model is proposed to speed up Ray Tracing process.
GPU benefits greatly from fixed depth subtree.
A hybrid model is proposed, to fully utilize compute power of CPU and GPU.
We demonstrate the capability of our method by producing Global Illumination effects for Bezier patches.

## Slide 50: Future Work
Work can be extended to higher order parametric surfaces like NURBS
KD-Trees as the top level hierarchy tree, could prove beneficial, especially for static scenes
Rearrangement of rays, in order to generate more coherence and hence greater speed-ups on the GPU
Our algorithm can be extended to faster and complex global illumination methods like photon mapping, bidirectional path tracing etc.

## Slide 51
Thank you

## Slide 52: Results
Intel i7 920 + Nvidia GT X580; 1024x1024